## Slide 1: Adaptive Control-Based Clock Synchronization in Wireless Sensor Networks
Kasım Sinan YILDIRIM*, Ruggero CARLI+, Luca SCHENATO+
* Department of Computer Engineering, Ege University, İzmir, TURKEY
+ Department of Information Engineering, University of Padova, Padova, ITALY
European Control Conference (ECC’15), Linz, Austria
July 17, 2015

## Slide 2: Outline
The Problem
Need for Synchronization
Proposed Solution
Control Theory
Results
Experiments
&
Discussion
Wireless Sensor Networks
Average Consensus
Challenges
Existing Solutions

## Slide 3: Wireless Sensor Networks
Hardware clock (built-in clock)
  Counter register
    Clocked with external crystal
      32kHz, 7.37 MHz nominal rate
    Read-only
Clock drift
  Deviation from the nominal rate
    30-100 parts per million (ppm)
    dependent on environmental factors such as:
      temperature, power supply, aging...
[Sommer et al. 2009]

## Slide 4: Need for Synchronization
Assigning global timestamps
  sensed data and events
  Coordinated actions
    Duty-cycling of the nodes for energy efficient operation
    Low-power, TDMA-based MAC layer
Applications
  Localization via time-of-flight measurements
  Tracking of moving objects

## Slide 5: Time Synchronization
Communicate
  Exchange current time information periodically
    Hardware clock value
Compute
  Calculate a logical clock
    Software function
    represents the global time
Challenge
  Measurement errors
  Message delay
    Deterministic and non-deterministic components
Send
Access
Transmission
Reception
Receive
0-100 ms
0-500 ms
1-10 ms
0-100 ms
timestamp
t
timestamp
Expected delay
Jitter
t
Frequency

## Slide 6: Pairwise Synchronization in Practice
Master – Slave Synchronization
  Collect (Hu,Hr) timestamp pairs periodically
  Employ least-squares regression
Hu
Hr
Beacon interval B
Reference Node r
Slave Node u
Linear relationship: Hr(t)=α+βHu(t)
clock offset
relative clock rate

## Slide 7: Least-Squares with Two Pairs
Slope:
Intercept:
Errors enter non-linearly to the equations!
Measurement errors
Measurement errors
Error contributed by
the transmission delays
Measurement errors
Measurement errors
Error contributed by
the transmission delays
The effect of various error sources appear as multiplicative noise!
Poor multi-hop performance scalability

## Slide 8: Time Synchronization as a Control Problem
e(t)
e(t+B)
Speed difference
input
time

## Slide 9: Proportional Control
P
steady state error
control instants
Compensates only initial offset differences

## Slide 10: Proportional-Integral Control
PI
Compensates both offset and clock speed differences
control instants

## Slide 11: PISync Algorithm - Pairwise Synchronization
Reference Clock Estimate
Convergence Conditions
Update Rule
Receive <Hr(tup)> at time tup from r
Calculate Error
Update Offset
Update Speed
Offset
Speed
Optimal Convergence Rate
No need to store received timestamps!
No regression table!
Very simple arithmetic operations!
Not the smallest steady-state error!
Integral gain should be adjusted adaptively!
Local time passed since update

## Slide 12: PISync Algorithm – Error Dynamics
For kP=1, PISync algorithm becomes
Measurement errors
Measurement errors
Error contributed by
the transmission delays
Error contributed by
the transmission delays
Errors enter linearly to the equations!
The effect of various error sources appear as additive noise!
Scalable multi-hop performance

## Slide 13: PISync - Integral Gain Adaptation
As kI gets smaller, we obtain smaller steady-state
error but longer convergence time!
Adaptation Rule
If e(h) > emax then kI = 0 (turn-off integrator)
Else if kI = kI*
Else if e(h)e(h-1)>0 then kI = max{2kI,kI*}
Else kI = kI/3
Maximum frequency
error
Inspired from [Yildirim and Gurcan et al. 2014]
Gradually increase or decrease according to the successive error signs

## Slide 14: PI control + Average Consensus
PI
No special reference node!
Nodes synchronize directly to their neighbors!
Clocks from neighboring nodes

## Slide 15: Testbed
Testbed setup
  20 MICAz sensor nodes
  FTSP (Flooding Time Synchronization Protocol [Marotti et al. 2004]) and PISync implemented in TinyOS 2.1
Network topology
  Line and grid topologies
Parameters
  Communication frequency: B=30 seconds
  Regression table of size 8 for FTSP
  fnom= 1 MHz
  kP=1 and 0 < kI < 2/(Bfnom)

## Slide 16: FTSP vs PISync
FTSP
FloodPISync
AvgPISync
FTSP
Completely blind operation!
No need to store neighbors time information explicitly!
Suitable for mobile networks!
Robust to packet losses
Very simple arithmetic operations
No need to store time information explicitly!
Scalable!

## Slide 17: PISync Complexity
FTSP
Just 15 Lines of TinyOS code!
 | FTSP | PISync
Error | ≈0.5 ms | 20 microseconds
RAM | 52 bytes | 16 bytes
ROM | 18000 bytes | 15432 bytes
CPU | 5.5 ms | 145 microseconds
20 times better performance!
50 times fewer operations!
4 times less RAM requirements!
Low power consumption!
Very easy to implement & code

## Slide 18: Conclusions
We considered time synchronization as a control problem
We solved this problem with a very simple and practical technique
  Proportional-Integral Controller
We introduced a new time synchronization protocol
  PISync
We observed
  Better performance scalability
  Less resource consumption
    Lower CPU and main memory overhead
    Lower power consumption
Notes: Motivate why clock synch is important

## Slide 19: Future Research Directions
Performance evaluation on real mobile networks
Implementation & evaluation of time-synchronized MAC layer
  Adaptive receiving window
  Evaluation of power consumption
Other algorithmic techniques?
  Better steady-state error & convergence
  Even lower resource requirements?

## Slide 20
Thank YOU!
Any Questions?