## Slide 1: Arithmetic/Logical Unit (ALU)
Digital Computer Design

## Slide 2: Arithmetic Circuits
Arithmetic circuits are the central building blocks of computers.
Computers and digital logic perform many arithmetic functions:
  addition, subtraction, comparisons, shifts, multiplication and division

## Slide 3: 1-Bit Adders

## Slide 4: Multibit Adders - Carry Propagate Adders (CPAs)
An N-bit adder sums two N-bit inputs A and B, and a carry in Cin to produce an N-bit result S and a carry out Cout.
Multibit adder is commonly called a carry propagate adder (CPA)
  because the carry out of one bit propagates into the next bit.

## Slide 5: CPAs: Ripple-Carry Adder
Chain together N full adders.
  The Cout of one stage acts as the Cin of the next stage
The ripple-carry adder is slow when N is large.
  For an 32-bit adder, S31 depends on C30, which depends on C29, which depends on C28, and so forth all the way back to Cin.

## Slide 6: CPAs: Ripple-Carry Adder
The fundamental reason that large ripple-carry adders are slow is that the carry signals must propagate through every bit in the adder.
tripple = NtFA
where tFA is the delay of a 1-bit full adder

## Slide 7: Subtracter
Subtraction is almost as easy:
  flip the sign of the second number, then add.
Flipping the sign of a two’ s complement number is done by inverting the bits and adding 1.

## Slide 8: Comparator: Equality
A comparator determines whether two binary numbers are equal or if one is greater or less than the other.

## Slide 9: Comparator: Less Than
Compute A − B and looking at the sign (most significant bit) of the result.
  If the result is negative (i.e., the sign bit is 1), then A is less than B. Otherwise A is greater than or equal to B.
This comparator, however, functions incorrectly upon overflow.
Sign bit

## Slide 10: Arithmetic/Logical Unit
ALU is one of the main components in the microprocessor.

## Slide 11: ALU: Arithmetic/Logical Unit
An Arithmetic/Logical Unit (ALU ) combines a variety of mathematical and logical operations into a single unit.
The ALU forms the heart of most computer systems.
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
The ALU receives a 2-bit control signal ALUControl that specifies which function to perform.

## Slide 12: ALU Implementation
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR

## Slide 13: ALU Implementation
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A OR B
ALUControl1:0 = 11
Mux selects output of OR gate as Result Result = A OR B

## Slide 14: ALU Implementation
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B
ALUControl1:0 = 00
Cin to adder = 0
2nd input to adder is B
Mux selects Sum as Result
Result = A + B

## Slide 15: ALU with Status Flags
Flag | Description
N | Result is Negative
Z | Result is Zero
C | Adder produces Carry out
V | Adder oVerflowed
Some ALUs produce extra outputs, called flags, that indicate information about the ALU output.

## Slide 16: ALU with Status Flags

## Slide 17: ALU with Status Flags: Negative
N = 1 if:
Result is negative
So, N is connected to most significant bit of Result

## Slide 18: ALU with Status Flags: Zero
Z = 1 if:
all of the bits of Result are 0

## Slide 19: ALU with Status Flags: Carry
C = 1 if:
Cout of Adder is 1 AND
ALU is adding or subtracting (ALUControl is 00 or 01)

## Slide 20: ALU with Status Flags: oVerflow
V = 1 if:
The addition of 2 same-signed numbers produces a result with the opposite sign. (the result is too big to fit in the available digits.)

## Slide 21: ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)

## Slide 22: ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs

## Slide 23: ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs
AND
A and B have same signs upon addition (ALUControl0 = 0)
OR
A and B have different signs upon subtraction
(ALUControl0 = 1)

## Slide 24: Shifters/Rotators
Shifters and rotators move bits and multiply or divide by powers of 2.
As the name implies, a shifter shifts a binary number left or right by a specified number of positions.
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100

## Slide 25: Shifters/Rotators
Arithmetic shifter: right shift, fills empty spaces with the old most significant bit (msb)
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111

## Slide 26: Example: Logical Shift Right Implementation
An N-bit shifter can be built from N N:1 multiplexers.
The input is shifted by 0 to N−1 bits, depending on the value of the log2N-bit select lines.
Depending on the value of the 2-bit shift amount shamt1:0, the output Y receives the input A shifted by 0 to 3 bits.
0 (Ground)

## Slide 27: Further Reading
  You can read Chapter 5 of your book
  From Section 5.1 to 5.2.5