## Slide 1: Instruction Encoding
Digital Computer Design

## Slide 2
How to Encode Instructions?
Assembly language is convenient for humans to read.
  However, digital circuits understand only 1’ s and 0’ s.
A program written in assembly language is to a representation using only 1’ s and 0’ s
  called Machine Language.
ARM uses a single instruction format
  32-bit instructions
    Variable-length instructions are avoided
      would add complexity.

## Slide 3: Design Principle 4
ARM defines three main instruction formats:
  (1) Data-processing
  (2) Memory
  (3) Branch
    Simpler decoder hardware
Number of instruction formats kept small
  smaller is faster

## Slide 4: Data-processing Instruction Format
The 32-bit instruction has six fields:
Operands:
  Rn: first source register
  Src2: second source – register or immediate
  Rd: destination register
Control fields:
  cond: specifies conditional execution
  op: the operation code or opcode
  funct: the function to perform

## Slide 5: Data-processing Control Fields
cond =11102 for unconditional execution
op = 002 for data-processing (DP) instructions
funct is composed of cmd, I-bit, and S-bit
  cmd: specifies the specific data-processing instruction. For example,
    cmd = 01002 for ADD
    cmd = 00102 for SUB
  I-bit
    I = 0: Src2 is a register
    I = 1: Src2 is an immediate
  S-bit: 1 if sets condition flags
    S = 0: SUB R0, R5, R7
    S = 1: ADDS R8, R2, R4 or CMP R3, #10

## Slide 6: Data-processing Src2 Variations
Three variations of Src2 encoding allow the second source operand to be
  Immediate
  Register
  Register-shifted register

## Slide 7: Data-processing instructions with three register operands
cond = 11102 (14) for unconditional execution
op = 002 (0) for data-processing instructions
cmd = 01002 (4) for ADD and 00102 (4) for SUB
Src2 is a register so I = 0

## Slide 8: Data-processing instructions with an immediate and two register operands
The immediate of the ADD instruction (42) can be encoded in 8 bits, so no rotation is needed (imm8=42, rot=0)
However, the immediate of SUB R2, R3, 0xFF0 cannot be encoded directly using the 8 bits of imm8 . Instead, imm8 is 255 (0xFF), and it is rotated right by 28 bits (rot = 14).
The right rotation by 28 bits is equivalent to a left rotation by 32− 28 = 4 bits.

## Slide 9: Shift instructions with immediate shift amounts
Shift Type | sh
LSL | 002
LSR | 012
ASR | 102
ROR | 112
cmd: field is 13 (11012) for all shift instruction
Rm: the second source operand
shamt5: the amount Rm is shifted
sh: the type of shift

## Slide 10: Shift instructions with register shift amounts
This instruction uses the register-shifted register addressing mode, where one register (Rm) is shifted by the amount held in a second register (Rs).

## Slide 11: Memory Instruction Format
Encodes: LDR, STR, LDRB, STRB
op = 012
Rn = base register
Rd = destination (load), source (store)
Src2 = offset: immediate or register (optionally shifted)
funct = I (immediate bar), P (preindex), U (add), B (byte), W (writeback), L (load)

## Slide 12: Memory Format funct Encodings
P | W | Indexing Mode
0 | 1 | Not supported
0 | 0 | Postindex
1 | 0 | Offset
1 | 1 | Preindex
Type of Operation
Value | I | U
0 | Immediate offset in Src2 | Subtract offset from base
1 | Register offset in Src2 | Add offset to base
Add/Subtract Immediate/Register Offset
Indexing Mode
L | B | Instruction
0 | 0 | STR
0 | 1 | STRB
1 | 0 | LDR
1 | 1 | LDRB

## Slide 13: Indexing Modes
Mode | Address | Base Reg. Update
Offset | Base register ± Offset | No change
Preindex | Base register ± Offset | Base register ± Offset
Postindex | Base register | Base register ± Offset
Examples
Offset: LDR R1, [R2, #4] ; R1 = mem[R2+4]
Preindex: LDR R3, [R5, #16]! ; R3 = mem[R5+16]
; R5 = R5 + 16
Postindex: LDR R8, [R1], #8 ; R8 = mem[R1]
    ; R1 = R1 + 8

## Slide 14: Memory Instruction Example
  Operation: mem[R5] <= R11; R5 = R5 - 26
  cond = 11102 (14) for unconditional execution
  op = 012 (1) for memory instruction
  funct = 00000002 (0)
  I = 0 (immediate offset), P = 0 (postindex),
  U = 0 (subtract), B = 0 (store word), W = 0 (postindex),
  L = 0 (store)
  Rd = 11, Rn = 5, imm12 = 26

## Slide 15: Branch Instruction Format
Encodes B and BL
op = 102
imm24: 24-bit immediate
funct = 1L2: L = 1 for BL, L = 0 for B

## Slide 16: Encoding Branch Target Address
Branch Target Address (BTA): The branch target address (BTA) is the address of the next instruction to execute if the branch is taken.
imm24 encodes BTA
imm24 = # of words BTA is away from PC+8

## Slide 17: Branch Instruction: Example 1
ARM assembly code
0xA0 BLT THERE
0xA4 ADD R0, R1, R2
0xA8 SUB R0, R0, R9
0xAC ADD SP, SP, #8
0xB0 MOV PC, LR
0xB4 THERE SUB R0, R0, #1
0xB8 BL TEST
PC = 0xA0
PC + 8 = 0xA8
THERE label is 3 instructions past PC+8
So, imm24 = 3
PC
PC+8
BTA

## Slide 18: Branch Instruction: Example 2
ARM assembly code
0x8040 TEST LDRB R5, [R0, R3]
0x8044 STRB R5, [R1, R3]
0x8048 ADD R3, R3, #1
0x8044 MOV PC, LR
0x8050 BL TEST
0x8054 LDR R3, [R1], #4
0x8058 SUB R4, R3, #9
PC = 0x8050
PC + 8 = 0x8058
TEST label is 6 instructions before PC+8
So, imm24 = -6
PC
PC+8
BTA

## Slide 19: Review: Condition Mnemonics
cond | Mnemonic | Name | CondEx
0000 | EQ | Equal | 
0001 | NE | Not equal | 
0010 | CS / HS | Carry set / Unsigned higher or same | 
0011 | CC / LO | Carry clear / Unsigned lower | 
0100 | MI | Minus / Negative | 
0101 | PL | Plus / Positive of zero | 
0110 | VS | Overflow / Overflow set | 
0111 | VC | No overflow / Overflow clear | 
1000 | HI | Unsigned higher | 
1001 | LS | Unsigned lower or same | 
1010 | GE | Signed greater than or equal | 
1011 | LT | Signed less than | 
1100 | GT | Signed greater than | 
1101 | LE | Signed less than or equal | 
1110 | AL (or none) | Always / unconditional | ignored

## Slide 20: Conditional Execution: Machine Code

## Slide 21: Interpreting Machine Code
Start with op: tells how to parse rest
    op = 00 (Data-processing)
    op = 01 (Memory)
    op = 10 (Branch)
I-bit: tells how to parse Src2
Data-processing instructions:
    If I-bit is 0, bit 4 determines if Src2 is a register (bit 4 = 0) or a register-shifted register (bit 4 = 1)
Memory instructions:
    Examine funct bits for indexing mode, instruction, and add or subtract offset

## Slide 22: Interpreting Machine Code: Example 1
0xE0475001
  Start with op: 002, so data-processing instruction
  I-bit: 0, so Src2 is a register
  bit 4: 0, so Src2 is a register (optionally shifted by shamt5)
  cmd: 00102 (2), so SUB
  Rn=7, Rd=5, Rm=1, shamt5 = 0, sh = 0
  So, instruction is: SUB R5,R7,R1

## Slide 23: Interpreting Machine Code: Example 2
0xE5949010
  Start with op: 012, so memory instruction
  funct: B=0, L=1, so LDR; P=1, W=0, so offset indexing; I=0, so immediate offset, U=1, so add offset
  Rn=4, Rd=9, imm12 = 16
  So, instruction is: LDR R9,[R4,#16]

## Slide 24: Power of the Stored Program
32-bit instructions & data stored in memory
Sequence of instructions: only difference between two applications
To run a new program:
  No rewiring required
  Simply store new program in memory
Program Execution:
  Processor fetches (reads) instructions from memory in sequence
  Processor performs the specified operation

## Slide 25: The Stored Program
Program Counter (PC): keeps track of current instruction

## Slide 26: Up Next
How to implement the ARM Instruction Set Architecture in Hardware?
  Microarchitecture

## Slide 27: Steps for translating and starting a program

## Slide 28: Memory MAP
The ARM architecture divides the address space into five parts or segments:
  the text segment
    stores the machine language program
  global data segment
    global variables that
  dynamic data segment
    the stack and the heap (dynamically allocated and deallocated)
  and segments for exception handlers, the operating system (OS) and input/output (I/O).

## Slide 29: Compiling a High-Level Program

## Slide 30: Further Reading
  You can read Chapter 6 of your book
  Section 6.4