## Slide 1: HDLs and SystemVerilog
Digital Computer Design

## Slide 2: Logic Arrays
Gates can be organized into regular arrays.
  If the connections are made programmable, these logic arrays can be configured to perform any function without the user having to connect wires in specific ways.
Software tools allow users to map logic designs onto these arrays.
Two types of logic arrays:
  programmable logic arrays (PLAs)
  field programmable gate arrays (FPGAs)

## Slide 3: A FPGA Board

## Slide 4: FPGA: Field Programmable Gate Array
FPGA is a reconfigurable substrate
  Reconfigurable functions
  Reconfigurable interconnection of functions
  Reconfigurable input/output (IO)
FPGAs fill the gap between software and hardware
  Achieves higher performance than software
  Maintains more flexibility than hardware

## Slide 5: LE: Logic Element
Composed of:
  LUTs (lookup tables): perform combinational logic
  Flip-flops: perform sequential logic
  Multiplexers: connect LUTs and flip-flops

## Slide 6: FPGA Architecture - Looking Inside an FPGA
Two main building blocks:
  Look-Up Tables (LUT) and Switches

## Slide 7: How Do We Program LUTs?
3-bit input LUT (3-LUT)
input (3 bits)
output (1 bit)
Data Input
Multiplexer (Mux): Selects one of the data input corresponding to select input
3
Select Input
000
001
010
011
100
101
110
111
3-LUT can implement any 3-bit input function

## Slide 8: An Example of Programming a LUT
Let’s implement a function that outputs ‘1’ when there are more than one ‘1’ in select inputs
input (3 bits)
output (1 bit)
Data Input
3
Configuration Memory
0
0
0
1
0
1
1
1
000
001
010
011
100
101
110
111

## Slide 9: How to Implement Complex Functions?
FPGAs are composed of a large number of LUTs and switches
FPGA Chip

## Slide 10: Advantages & Disadvantages of FPGAs
Advantages
  Low development cost
  Short time to market
  Reconfigurable in the field
  Reusability
  An algorithm can be implemented directly in hardware
    No ISA, high specialization
Disadvantages
  Not as fast and power efficient as application specific hardware
  Reconfigurability adds significant area overhead

## Slide 11: Computer-Aided Design (CAD) Tools
FPGAs have many resources (e.g., LUTs, switches)
They are hard to program manually
How can we
  represent a high-level functional description of our hardware circuit using the FPGA resources?
  select the resources to map our circuit to?
  optimally configure the interconnect between the selected resources?
  generate a final configuration file to properly configure an FPGA?

## Slide 12: FPGA Design Flow
Problem Definition
Hardware Description Language (HDL)
Verilog, VHDL
Your task!
Logic Synthesis
Placement and Routing
Bitstream Generation
Programming the FPGA
Xilinx Vivado

## Slide 13: Hardware description language (HDL)
Specifies logic function only
  Computer-aided design (CAD) tool produces or synthesizes the optimized gates
  Think of the hardware the HDL should produce!
Most commercial designs built using HDLs
Two leading HDLs:
  SystemVerilog
    developed in 1984 by Gateway Design Automation
    IEEE standard (1364) in 1995
    Extended in 2005 (IEEE STD 1800-2009)
  VHDL 2008
    Developed in 1981 by the Department of Defense
    IEEE standard (1076) in 1987
    Updated in 2008 (IEEE STD 1076-2008)

## Slide 14: HDL to Gates
Simulation
  Inputs applied to circuit
  Outputs checked for correctness
  Millions of dollars saved by debugging in simulation instead of hardware
Synthesis
  Transforms HDL code into a netlist describing the hardware (i.e., a list of gates and the wires connecting them)

## Slide 15: SystemVerilog Modules
A block of hardware with inputs and outputs is called a module.
Two types of Modules:
  Behavioral: describe what a module does
  Structural: describe how it is built from simpler modules

## Slide 16: Behavioral SystemVerilog
module/endmodule: required to begin/end module
example: name of the module
Operators:
  ~: NOT
  &: AND
  |: OR
module example(input logic a, b, c,
output logic y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule

## Slide 17: HDL Simulation
module example(input logic a, b, c,
output logic y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule
  Inputs applied to circuit, Outputs checked for correctness

## Slide 18: HDL Synthesis
module example(input logic a, b, c,
output logic y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule
  Transforms HDL code into a netlist describing the hardware (i.e., a list of gates and the wires connecting them)

## Slide 19: Further Reading
  You can read Chapter 4 of your book.