## Slide 1: Microarchitecture
Digital Computer Design

## Slide 2: Introduction
Microarchitecture: how to implement an architecture in hardware
Processor:
  Datapath: operates on words of data. It contains structures such as memories, registers, ALUs, and multiplexers.
  Control: receives the current instruction from the datapath and tells the datapath how to execute that instruction.

## Slide 3: Single-Cycle Processor
Executes instructions in a single cycle
  Datapath: state elements with combinational logic that can execute the various instructions
  Control signals: determine which specific instruction is performed by the datapath at any given time.
  The control unit: contains combinational logic that generates the appropriate control signals based on the current instruction.
Fetch -> Decode -> Execute

## Slide 4: ARM Architectural State Elements

## Slide 5: ARM Architectural State Elements
PC points to the current instruction.
  Its input, PC′, indicates the address of the next instruction.
The instruction memory has a single read port.
  takes a 32-bit instruction address input, A
  reads the 32-bit data (i.e., instruction) from that address onto the read data output, RD.
The data memory has a single read/write port.
  If its write enable, WE, is asserted, then it writes data WD into address A on the rising edge of the clock.
  If its write enable is 0, then it reads address A onto RD.

## Slide 6: ARM Processor
Consider subset of ARM instructions:
  Data-processing instructions:
    ADD, SUB, AND, ORR
    with register and immediate Src2, but no shifts
  Memory instructions:
    LDR, STR
    with positive immediate offset
  Branch instructions:
    B

## Slide 7: Single-Cycle ARM Processor
Example: LDR R1, [R2, #5]
LDR Rd, [Rn, imm12]

## Slide 8: Single-Cycle Datapath: LDR fetch
STEP 1: Fetch instruction

## Slide 9: Single-Cycle Datapath: LDR Reg Read
STEP 2: Read source operands from Register File
LDR Rd, [Rn, imm12]

## Slide 10: Single-Cycle Datapath: LDR Immed.
STEP 3: Extend the immediate
LDR Rd, [Rn, imm12]

## Slide 11: Single-Cycle Datapath: LDR Address
STEP 4: Compute the memory address
LDR Rd, [Rn, imm12]

## Slide 12: Single-Cycle Datapath: LDR Mem Read
LDR Rd, [Rn, imm12]
STEP 5: Read data from memory and write it back to register file

## Slide 13: Single-Cycle Datapath: PC Increment
STEP 6: Determine address of next instruction

## Slide 14: Single-Cycle Datapath: Access to PC
PC can be source/destination of instruction
Source: R15 must be available in Register File
  in the ARM architecture, reading register R15 returns PC + 8.
Destination: Be able to write result to PC

## Slide 15: Single-Cycle Datapath: STR
Expand datapath to handle STR:
Write data in Rd to memory
STR Rd, [Rn, imm12]

## Slide 16: Single-Cycle Datapath: Data-processing
With immediate Src2:
Read from Rn and Imm8 (ImmSrc chooses the zero-extended Imm8 instead of Imm12)
Write ALUResult to register file
Write to Rd
ADD Rd, Rn, imm8

## Slide 17: Single-Cycle Datapath: Data-processing
With immediate Src2:
Read from Rn and Imm8 (ImmSrc chooses the zero-extended Imm8 instead of Imm12)
Write ALUResult to register file
Write to Rd
ADD Rd, Rn, imm8

## Slide 18: Single-Cycle Datapath: Data-processing
With register Src2:
Read from Rn and Rm (instead of Imm8)
Write ALUResult to register file
Write to Rd
ADD Rd, Rn, Rm

## Slide 19: Single-Cycle Datapath: Data-processing
With register Src2:
Read from Rn and Rm (instead of Imm8)
Write ALUResult to register file
Write to Rd
ADD Rd, Rn, Rm

## Slide 20: Single-Cycle Datapath: B
Calculate branch target address:
BTA = (ExtImm) + (PC + 8)
ExtImm = Imm24 << 2 and sign-extended
B Label

## Slide 21: Single-Cycle Datapath: ExtImm
ImmSrc1:0 | ExtImm | Description
00 | {24’b0, Instr7:0} | Zero-extended imm8
01 | {20’b0, Instr11:0} | Zero-extended imm12
10 | {6{Instr23}, Instr23:0} | Sign-extended imm24

## Slide 22: Single-Cycle ARM Processor

## Slide 23: Single-Cycle Control

## Slide 24: Single-Cycle Control
These signals change the state (PC, RF, Memory)
If instruction shouldn’t execute, forced to 0
Sent through
Conditional Logic
first, then to
datapath
Sent directly
to datapath

## Slide 25: Single-Cycle Control
FlagW1:0: Flag Write signal, asserted when ALUFlags should be saved (i.e., on instruction with S=1)
ADD, SUB update all flags (NZCV)
AND, ORR only update NZ flags
So, two bits needed:
  FlagW1 = 1: NZ saved (ALUFlags3:2 saved)
  FlagW0 = 1: CV saved (ALUFlags1:0 saved)

## Slide 26: Single-Cycle Control: Decoder

## Slide 27: Single-Cycle Control: Decoder
Submodules:
Main Decoder
ALU Decoder
PC Logic

## Slide 28: Single-Cycle Control: Decoder
Submodules:
Main Decoder
ALU Decoder
PC Logic

## Slide 29: Control Unit: Main Decoder
Op | Funct5 | Funct0 | Type | Branch | MemtoReg | MemW | ALUSrc | ImmSrc | RegW | RegSrc | ALUOp
00 | 0 | X | DP Reg | 0 | 0 | 0 | 0 | XX | 1 | 00 | 1
00 | 1 | X | DP Imm | 0 | 0 | 0 | 1 | 00 | 1 | X0 | 1
01 | X | 0 | STR | 0 | X | 1 | 1 | 01 | 0 | 10 | 0
01 | X | 1 | LDR | 0 | 1 | 0 | 1 | 01 | 1 | X0 | 0
11 | X | X | B | 1 | 0 | 0 | 1 | 10 | 0 | X1 | 0

## Slide 30: Single-Cycle Control: Decoder
Submodules:
Main Decoder
ALU Decoder
PC Logic

## Slide 31: Review: ALU
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR

## Slide 32: Review: ALU

## Slide 33: Control Unit: ALU Decoder
ALUOp | Funct4:1 (cmd) | Funct0 (S) | Type | ALUControl1:0 | FlagW1:0
0 | X | X | Not DP | 00 | 00
1 | 0100 | 0 | ADD | 00 | 00
 |  | 1 |  |  | 11
 | 0010 | 0 | SUB | 01 | 00
 |  | 1 |  |  | 11
 | 0000 | 0 | AND | 10 | 00
 |  | 1 |  |  | 10
 | 1100 | 0 | ORR | 11 | 00
 |  | 1 |  |  | 10
  FlagW1 = 1: NZ (Flags3:2) should be saved
  FlagW0 = 1: CV (Flags1:0) should be saved

## Slide 34: Single-Cycle Control: Decoder
Submodules:
Main Decoder
ALU Decoder
PC Logic

## Slide 35: Single-Cycle Control: PC Logic
PCS = 1 if PC is written by an instruction or branch (B):
PCS = ((Rd == 15) & RegW) | Branch
If instruction is executed: PCSrc = PCS
Else PCSrc = 0 (i.e., PC = PC + 4)

## Slide 36: Single-Cycle Control: Cond. Logic

## Slide 37: Conditional Logic
Function:
Check if instruction should execute (if not, force PCSrc, RegWrite, and MemWrite to 0)
Possibly update Status Register (Flags3:0)

## Slide 38: Conditional Logic
Function:
Check if instruction should execute (if not, force PCSrc, RegWrite, and MemWrite to 0)
Possibly update Status Register (Flags3:0)

## Slide 39: Conditional Logic: Conditional Execution
Depending on condition mnemonic (Cond3:0) and condition flags (Flags3:0) the instruction is executed (CondEx = 1)
Flags3:0 is the status register

## Slide 40: Conditional Logic: Conditional Execution
Cond3:0 | Mnemonic | Name | CondEx
0000 | EQ | Equal | 
0001 | NE | Not equal | 
0010 | CS / HS | Carry set / Unsigned higher or same | 
0011 | CC / LO | Carry clear / Unsigned lower | 
0100 | MI | Minus / Negative | 
0101 | PL | Plus / Positive of zero | 
0110 | VS | Overflow / Overflow set | 
0111 | VC | No overflow / Overflow clear | 
1000 | HI | Unsigned higher | 
1001 | LS | Unsigned lower or same | 
1010 | GE | Signed greater than or equal | 
1011 | LT | Signed less than | 
1100 | GT | Signed greater than | 
1101 | LE | Signed less than or equal | 
1110 | AL (or none) | Always / unconditional | ignored
Review: Condition Mnemonics

## Slide 41: Conditional Logic: Conditional Execution
Example: AND R1, R2, R3
Cond3:0=1110 (unconditional) => CondEx = 1
Flags3:0 = NZCV

## Slide 42: Conditional Logic: Conditional Execution
Example: EOREQ R5, R6, R7
Cond3:0=0000 (EQ): if Flags3:2=0100 => CondEx = 1
Flags3:0 = NZCV

## Slide 43: Conditional Logic
Function:
Check if instruction should execute (if not, force PCSrc, RegWrite, and MemWrite to 0)
Possibly update Status Register (Flags3:0)

## Slide 44: Conditional Logic: Update (Set) Flags
Flags3:0 updated (with ALUFlags3:0) if:
FlagW is 1 (i.e., the instruction’s S-bit is 1) AND
CondEx is 1 (the instruction should be executed)
Flags3:0 = NZCV

## Slide 45: Conditional Logic: Update (Set) Flags
Recall:
ADD, SUB update all Flags
AND, OR update NZ only
So Flags status register has two write enables: FlagW1:0

## Slide 46: Review: ALU Decoder
ALUOp | Funct4:1 (cmd) | Funct0 (S) | Type | ALUControl1:0 | FlagW1:0
0 | X | X | Not DP | 00 | 00
1 | 0100 | 0 | ADD | 00 | 00
 |  | 1 |  |  | 11
 | 0010 | 0 | SUB | 01 | 00
 |  | 1 |  |  | 11
 | 0000 | 0 | AND | 10 | 00
 |  | 1 |  |  | 10
 | 1100 | 0 | ORR | 11 | 00
 |  | 1 |  |  | 10
  FlagW1 = 1: NZ (Flags3:2) should be saved
  FlagW0 = 1: CV (Flags1:0) should be saved

## Slide 47: Conditional Logic: Update (Set) Flags
All Flags updated
Example: SUBS R5, R6, R7
FlagW1:0 = 11 AND CondEx = 1 (unconditional) => FlagWrite1:0 = 11

## Slide 48: Conditional Logic: Update (Set) Flags
Flags3:0 = NZCV
Only Flags3:2 updated
i.e., only NZ Flags updated
Example: ANDS R7, R1, R3
FlagW1:0 = 10 AND CondEx = 1 (unconditional) => FlagWrite1:0 = 10

## Slide 49: Example: ORR

## Slide 50: Extended Functionality: CMP

## Slide 51: Extended Functionality: CMP
No change to datapath

## Slide 52: Extended Functionality: CMP

## Slide 53: Extended Functionality: CMP
ALUOp | Funct4:1 (cmd) | Funct0 (S) | Type | ALUControl1:0 | FlagW1:0 | NoWrite
0 | X | X | Not DP | 00 | 00 | 0
1 | 0100 | 0 | ADD | 00 | 00 | 0
 |  | 1 |  |  | 11 | 0
 | 0010 | 0 | SUB | 01 | 00 | 0
 |  | 1 |  |  | 11 | 0
 | 0000 | 0 | AND | 10 | 00 | 0
 |  | 1 |  |  | 10 | 0
 | 1100 | 0 | ORR | 11 | 00 | 0
 |  | 1 |  |  | 10 | 0
 | 1010 | 1 | CMP | 01 | 11 | 1

## Slide 54: Extended Functionality: Shifted Register

## Slide 55: Processor Performance
Program execution time
Execution Time = (#instructions)(cycles/instruction)(seconds/cycle)
# instructions x CPI x TC
Definitions:
  CPI: cycles per instruction (Cycles/instruction)
  clock period: seconds/cycle
  IPC: instructions per cycle (instructions/cycle)
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance

## Slide 56: Single-Cycle Performance
TC limited by critical path (LDR)

## Slide 57: Single-Cycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Decoder | tdec | 70
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 58: Single-Cycle Performance Example
  Tc1 = tpcq_PC + 2tmem + tdec + tRFread + tALU + 2tmux + tRFsetup
= [50 + 2(200) + 70 + 100 + 120 + 2(25) + 60] ps
= 840 ps
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Decoder | tdec | 70
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 59: Single-Cycle Performance Example
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC
= (100 × 109)(1)(840 × 10-12 s)
= 84 seconds

## Slide 60: Multicycle ARM Processor
Single-cycle:
  + simple
  cycle time limited by longest instruction (LDR)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle processor addresses these issues by breaking instruction into shorter steps
  shorter instructions take fewer steps
  can re-use hardware
  cycle time is faster

## Slide 61: Multicycle ARM Processor
Single-cycle:
  + simple
  cycle time limited by longest instruction (LDR)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times

## Slide 62: Reading
  Chapter 7
  Sections 7.1, 7.2 and 7.3