## Slide 1: Counters, Shift Registers, Memory Arrays
Digital Computer Design

## Slide 2: Counters
Increments on each clock edge
Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays

## Slide 3: Shift Registers
Shift a new bit in on each clock edge
Shift a bit out on each clock edge
Serial-to-parallel converter: converts serial input (Sin) to parallel output (Q0:N-1)
Implementation:
Symbol:

## Slide 4: Shift Register with Parallel Load
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)

## Slide 5: Memory Arrays
Efficiently store large amounts of data
3 common types:
  Dynamic random access memory (DRAM)
  Static random access memory (SRAM)
  Read only memory (ROM)
M-bit data value read/written at each unique N-bit address

## Slide 6: Memory Arrays
2-dimensional array of bit cells
Each bit cell stores one bit
N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M

## Slide 7: Memory Array Example
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100

## Slide 8: Memory Arrays
How many words? Word size?

## Slide 9: Addressing Memory
Let’s implement a simple memory array with:
3-bit addressability & address space size of 2 (total of 6 bits)
D
Q
WE
1 Bit
Bit2
Bit1
Bit0
Bit2
Bit1
Bit0
Addr(0)
Addr(1)
6-Bit Memory Array
Notes: Memory array

## Slide 10: Reading from Memory
How can we select the address to read?
Because there are 2 addresses, address size is log(2)=1 bit
Notes: How do we read from memory?

## Slide 11: Reading from Memory
D[2]
D[1]
D[0]
Addr[0]
Wordline
How can we select the address to read?
Because there are 2 addresses, address size is log(2)=1 bit

## Slide 12: Reading from Memory
Address Decoder
D[2]
D[1]
D[0]
Addr[0]
Wordline
How can we select the address to read?
Because there are 2 addresses, address size is log(2)=1 bit

## Slide 13: Reading from Memory
Address Decoder
D[2]
D[1]
D[0]
Addr[0]
Multiplexer
Wordline
How can we select the address to read?
Because there are 2 addresses, address size is log(2)=1 bit

## Slide 14: Writing to Memory
How can we select the address and write to it?
Notes: How can we write to memory?

## Slide 15: Writing to Memory
How can we select the address and write to it?
Input is indicated with Di
Di[2]
Di[1]
Di[0]
Addr[0]
WE

## Slide 16: Putting it all Together
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[0]
WE
Enable reading and writing to a memory array
Notes: Putting it all together...

## Slide 17: A Bigger Memory Array
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[1:0]
WE
Notes: A bigger memory array

## Slide 18: A Bigger Memory Array
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[1:0]
WE
Address Decoder
Multiplexer

## Slide 19: Multi-ported Memories
Multiported memories can access several addresses simultaneously
Example: 3-ported memory
  2 read ports (A1/RD1, A2/RD2)
  1 write port (A3/WD3, WE3 enables writing)
Register file: small multi-ported memory

## Slide 20: Types of Memory
Memories are classified based on how they store bits in the bit cell.
  Random access memory (RAM):
    volatile: loses its data when power off
    called random access memory because any data word is accessed with the same delay as any other.
    e.g. main memory in computers
  Read only memory (ROM):
    nonvolatile: retains data when power off
    e.g. flash memory in cameras

## Slide 21: Types of RAM
DRAM (Dynamic random access memory)
SRAM (Static random access memory)
Differ in how they store data:
  DRAM uses a capacitor
  SRAM uses cross-coupled inverters

## Slide 22: Dynamic Random Access Memory (DRAM)
Data bits stored on capacitor
  When the capacitor is charged to VDD the stored bit is 1
  When it is discharged to GND the stored bit is 0
The transistor behaves as a switch
  either connects or disconnects the capacitor from the bitline.

## Slide 23: Dynamic Random Access Memory (DRAM)
Dynamic because the value needs to be refreshed (rewritten) periodically and after read:
  Charge leakage from the capacitor degrades the value
  Reading destroys the stored value
    Data word must be restored (rewritten) after each read.

## Slide 24: Static Random Access Memory (SRAM)
Static because stored bits do not need to be refreshed.
  Unlike DRAM, if noise degrades the value of the stored bit, the cross-coupled inverters restore the value.
DRAM bit cell:
SRAM bit cell:

## Slide 25: Area and Delay
The data bit stored in a flip-flop is available immediately at its output.
  But flip-flops take at least 20 transistors to build.
DRAM latency is longer than that of SRAM
  Because its bitline is not actively driven by a transistor.
  DRAM must wait for charge to move (relatively) slowly from the capacitor to the bitline.

## Slide 26: Read Only Memory ROM
Read only memory (ROM) stores a bit as the presence or absence of a transistor.
  If the transistor is present, it pulls the bitline LOW.
  If it is absent, the bitline remains HIGH.
The contents of the ROM bit are specified during manufacturing by the presence or absence of a transistor in each bit cell.

## Slide 27: Read Only Memory ROM
A programmable ROM (PROM) places a transistor in every bit cell
  but provides a way to connect or disconnect the transistor to ground.
A fuse-programmable ROM allows user programs to selectively blow fuses by applying a high voltage.

## Slide 28: Read Only Memory ROM
Erasable PROMs (EPROMs) replace the transistor and fuse with a floating-gate transistor.
  The floating gate is not physically attached to any other wires.
    When suitable high voltages are applied, transistor is connects to the bitline to the wordline.
    When the EPROM is exposed to intense ultraviolet (UV) light for about half an hour, the transistor is disconnected.
    These actions are called programming and erasing, respectively.

## Slide 29: Read Only Memory ROM: Dot Notation

## Slide 30: Logic with Memory Arrays
Although they are used primarily for data storage, memory arrays can also perform combinational logic functions.
A 2N-word x M-bit memory can perform any combinational function of N inputs and M outputs.
  X = AB
  Y = A + B
  Z = A B

## Slide 31: Logic with Memory Arrays
Called lookup tables (LUTs): look up output at each input combination (address)

## Slide 32: Logic with Memory Arrays
Data2 = A1 xor A0
Data1 = A1 + A0
Data0 = A1A0

## Slide 33: Further Reading
  You can read Chapter 5 of your book
  Sections 5.4 and 5.5