## Slide 1: Synchronous Sequential Circuit Design
Digital Computer Design

## Slide 2: Races and Instability
Combinational logic
  has no cyclic paths and no races
  If inputs are applied to combinational logic, the outputs will always settle to the correct value within a propagation delay.
Sequential circuits with cyclic paths
  If there is a cyclic path, undesirable races or unstable behavior might occur.

## Slide 3: Example-1: Asynchronous Sequential Circuit
A problematic circuit: (no clock)
  No inputs and 1-3 outputs
  Astable circuit, oscillates
  Period depends on inverter delay
  It has a cyclic path: output fed back to input
  The behavior of the asynchronous circuit depends on the gate delays.

## Slide 4: Example-2: Asynchronous Sequential Circuit
A problematic circuit (with clock):
Suppose CLK=D= 1.
  Keeps Q=1.
Bur if the inverter delay is longer than that of the AND and OR gates:
  When CLK becomes 0, Q becomes stuck at 0.

## Slide 5: Synchronous Sequential Circuits
Breaks cyclic paths by inserting registers
  Registers contain state of the system
  All registers receive the same clock signal
  Every cyclic path contains at least one register
State changes at clock edge: system synchronized to the clock
A flip-flop is the simplest synchronous sequential circuit.

## Slide 6: Circuit Examples
Which of the circuits are synchronous sequential circuits?
Sequential circuits that are not synchronous are asynchronous.

## Slide 7: Synchronous Sequential Circuit Design
Synchronous sequential circuits can be drawn in FSM form.
A FSM consists of two blocks of combinational logic:
  next state logic
  output logic
  Moore FSM: outputs depend only on current state
  Mealy FSM: outputs depend on current state and inputs

## Slide 8: Traffic Light Controller Design
  Traffic sensors: TA, TB (TRUE when there’s traffic)
  Lights: LA, LB

## Slide 9: 1- Determine Input and Output Signals
  Traffic sensors: TA, TB (TRUE when there’s traffic)
  Lights: LA, LB
Inputs: CLK, Reset, TA, TB
Outputs: LA, LB

## Slide 10: 2- Obtain State Transition Diagram
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs

## Slide 11: 2- Obtain State Transition Diagram
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs

## Slide 12: 3- From State Transition Diagram to State Transition Table
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
State Transition Table

## Slide 13: 4- State Encoding
The state transition diagram is abstract in that it uses states labeled S0, S1, S2, S3.
  To build a real circuit, the states and outputs must be assigned binary encodings.
Each state is encoded with two bits: S1:0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11

## Slide 14: 5- Encoded State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
State Transition Table
Encoded State Transition Table

## Slide 15: 6- Register (Flip-Flop) Input Equations (Next State Logic)
The equations can also be simplified using Karnaugh maps:
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
S’1 = (S1 ∙ S0) + (S1 ∙ S0 ∙ TB) + (S1 ∙ S0 ∙ TB)
S’0 = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)
S’1 = S1 xor S0
Flip-Flop (register) Input Equations:

## Slide 16: Circuit Schematic: Next State Logic

## Slide 17: Circuit Schematic: Next State Logic

## Slide 18: 7- Output Table and Output Equations (Output Logic)
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1
LB0 = S1 ∙ S0
Output Equations:
Output Table

## Slide 19: Circuit Schematic: Output Logic

## Slide 20: One-Hot State Encoding
Binary encoding:
  i.e., for four states, 00, 01, 10, 11
  K states only needs log2K bits of state
One-hot encoding
  One state bit per state
  K states only needs K bits of state
  Only one state bit HIGH at once
  i.e., for 4 states, 0001, 0010, 0100, 1000
  Requires more flip-flops
  Often next state and output logic is simpler
State | Binary Encoding
S0 | 00
S1 | 01
S2 | 10
State | One Hot Encoding |  | 
 | S2 | S1 | S0
S0 | 0 | 0 | 1
S1 | 0 | 1 | 0
S2 | 1 | 0 | 0

## Slide 21: A divide-by-N Counter Design With One Hot State Encoding
The output Y is HIGH for one clock cycle out of every N.
Divide-by-3 counter
Current State | Next State
S0 | S1
S1 | S2
S2 | S0
Current State | Output
S0 | 1
S1 | 0
S2 | 0
State Transition Table
Output Table

## Slide 22: State Table, Output Table, State Encoding
State | One Hot Encoding |  | 
 | S2 | S1 | S0
S0 | 0 | 0 | 1
S1 | 0 | 1 | 0
S2 | 1 | 0 | 0
State Encoding
Current State |  |  | Next State |  | 
S2 | S1 | S0 | S’2 | S’1 | S’0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1
Encoded State Table
Current State |  |  | Output
S2 | S1 | S0 | Y
0 | 0 | 1 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
Encoded Output Table

## Slide 23: Register Input Equations and Output Equations
It is easy to derive boolean equations with One-Hot encoding.
Current State |  |  | Next State |  | 
S2 | S1 | S0 | S’2 | S’1 | S’0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1
S’2=S1
S’1=S0
S’0=S
Encoded State Table
Current State |  |  | Output
S2 | S1 | S0 | Y
0 | 0 | 1 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
Output Table
Flip-Flop (register) Input Equations:
Y=S0
Output Equations:

## Slide 24: Pattern Recognizer Design
A synchronous sequential circuit that recognizes the occurrence of 01 by observing a given sequence.
  0010101000101010001010010001
  Outputs 1 when the patter is found.
Design Steps:
  Determine Input and Output Signals
  Draw State Transition Diagram
  State Transition Table
  Encoded State Transition Table
  Register Input Equations
  Encoded Outputs
  Output Equations
  Draw Schematic

## Slide 25: State Transition Diagrams

## Slide 26: Moore State Transition and Output Tables
Current State | Input | Next State
S | A | S’
S0 | 0 | S1
S0 | 1 | S0
S1 | 0 | S1
S1 | 1 | S2
S2 | 0 | S1
S2 | 1 | S0
Current State | Output
S | Y
S0 | 0
S1 | 0
S2 | 1

## Slide 27: State Transition and Output Tables with State Encoding
Current State |  | Input | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0
Current State |  | Output
S1 | S0 | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1

## Slide 28: Register Input Equations and Output Equations
S’1 = S0A
S’0 = A
Y = S1
Current State |  | Input | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0
Current State |  | Output
S1 | S0 | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1

## Slide 29: Mealy State Transition and Output Tables
Current State | Input | Next State | Output
S | A | S’ | Y
S0 | 0 | S1 | 0
S0 | 1 | S0 | 0
S1 | 0 | S1 | 0
S1 | 1 | S2 | 1

## Slide 30: State Transition and Output Tables with State Encodings
Current State | Input | Next State | Output
S | A | S’ | Y
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 31: Register Input Equations and Output Equations
S’0 = A
Y = S0 A
Current State | Input | Next State | Output
S | A | S’ | Y
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 32: Circuit Schematic
Moore Machine
Mealy Machine

## Slide 33: Further Reading
  These slides are sufficient to understand the design of the synchronous sequential circuits.
  You can read Chapter 3 of your book
  Sections 3.2, 3.3, 3.5